## Slide 1: Supersonic Gas Ejector Design and Performance Evaluation Muhammad Hazim Bin Sulaiman (A0155095B)

## Slide 2: Content
Introduction to Supersonic Gas Ejectors
Problem Statement
ESDU 84029
Methodology
Results and Discussion
Methane
Performance evaluation
Conclusion and Future Work

## Slide 3: Introduction to Supersonic Gas Ejectors
Gas ejectors are used in many appliances throughout many industries. It is an appliance that draws the pressure energy from a high-pressure motive stream to entrain the low pressure stream from a secondary source

## Slide 4
Notes: velocity change in area equation for isentropic flow

## Slide 7
Notes: Recover pressure

## Slide 8
Other subscripts
e – primary nozzle exit
th – primary nozzle throat
“ – secondary stream
‘ – primary stream
Main subscripts
0 – secondary flow entry plane
1 – primary nozzle entry plane
2 – primary nozzle exit plane
3 – mixing duct entry plane
4 – mixing duct exit plane
5 – diffuser exit plane
Notes: Vital planes and areas are denoted from 0 to 5

## Slide 9: Problem Statement
Investigate the design conditions of a supersonic gas ejector with methane as a medium
Design condition is set to be the best diffuser diameter that outputs the highest pressure past the diffuser exit
The mathematical model will then be used for performance evaluation

## Slide 10: ESDU 84029
Ejectors and jet pumps: Design and performance for compressible flow
Quick Design Method and Detailed Design Method
However, these methods are only applicable if the medium is air
Equations are provided in the appendix of the ESDU84029 that are used to find the pressures within the gas ejector

## Slide 11: Methodology
Operating Conditions
Fixed Parameters
Equations
Calculations

## Slide 12: Operating Conditions
Primary |  | Secondary |  | Mixing Duct | 
Tp (in Celsius) | 25 | Ts (in Celsius) | 25 | T4 (in Celsius) | 25
Tp (in Kelvin) | 298 | Ts (in Kelvin) | 298 | T4 (in Kelvin) | 298
P1 (in Pa) | 5.00E+05 | P0 (in Pa) | 4.00E+04 |  | 
Mass FR (in kg/s) | 1 | Mass FR (in kg/s) | 0.2 | Mass FR (in m3/s) | 1.2
Volumetric FR (in m3/s) | 1.225 | Volumetric FR (in m3/s) | 0.245 |  | 

## Slide 13: Fixed Parameters
Diameters (in mm) |  | Areas (in m^2) | 
D0 | 200 | A0 | 0.031415
D1 | 60 | A1 | 0.002827
Dth | 23.97252 | Ath | 0.000451
De | 33.90226 | Ae | 0.000903
D2 | 100 | A2 | 0.007854
D3 | 150 | A3 | 0.017671
D3' | 33.90226 | A3’ | 0.000903
D3" | 116.0977 | A3” | 0.010586
D4 | 150 | A4 | 0.017671
D5(to be varied) | - | A5 | -
Other subscripts
e – primary nozzle exit
th – primary nozzle throat
“ – secondary stream
‘ – primary stream
Main subscripts
0 – secondary flow entry plane
1 – primary nozzle entry plane
2 – primary nozzle exit plane
3 – mixing duct entry plane
4 – mixing duct exit plane
5 – diffuser exit plane

## Slide 14: Equations
Secondary flow intake continuity equation
Primary nozzle continuity equation

## Slide 15: Equations
Mixing duct continuity equation
Diffuser Bernoulli equation

## Slide 16: Calculations
Calculations are done through excel
Physical variables of air is used first and validated
Following that, values of methane are used

## Slide 17: Results
Graph of diffuser exit pressure (Pt5) against diffuser diameter (D5)
Validation
  Cross-check to values found in ESDU 84029
Methane
  Translate physical values to methane values

## Slide 18: Graph of diffuser exit pressure (Pt5) against diffuser diameter (D5)
Maximum pressure: 124100 Pa
Chosen diameter: 220mm
  124000Pa (99.9% efficiency)

## Slide 19: Validation
Graph of Optimum Performance Relationship Between Pressure Ratios and Mass Flow Ratio from ESDU 84029
 | Expected (Obtained from ESDU 84029) | Calculated
Pt1/Pt5 | 4 | 4.04
Pt5/Pt0 | 3.2 | 3.1

## Slide 20: Methane
Maximum pressure: 121900 Pa
Chosen diameter: 185 mm
  121656 Pa (99.8% efficiency)

## Slide 21: Performance Evaluation
Mathematical model is set in the excel sheet
By changing values of dimensions, operating conditions and physical variables (eg. Specific heat ratio & Density), the corresponding graph will be produced

## Slide 22: Conclusion
Investigate the design conditions of a supersonic gas ejector with methane as a medium
Design condition is set to be the best diffuser diameter that outputs the highest pressure past the diffuser exit
The mathematical model will then be used for performance evaluation
Future work
  CFD
  Physical experiment

## Slide 23: Thank You

## Slide 24: Flow Chart
Primary nozzle continuity equation
Input Pt1 to obtain Pt3”
Secondary flow intake continuity equation
Input Pt0 to obtain Pt3’
Mixing duct continuity equation
Input Pt3’ & Pt3” to obtain Pt4
Diffuser continuity equation
Input Pt4 and vary D5 to obtain Pt5

## Slide 28
Static pressure based mass flow function
Velocity of sound
Mach number
Area ratio equation for compressible flow

## Slide 29
 | Expected (Obtained from ESDU 84029) | Calculated
Pt1/Pt5 | 4 | 4.04
Pt5/Pt0 | 3.2 | 3.1